CAN TOOLS

---
The python-can library provides Controller Area Network support for Python, providing common abstractions to different hardware devices, and a suite of utilities for sending and receiving messages on a CAN bus.

---
CAN TOOLS
Parsing of Files such as,
DBC (Data base Container)
KCD (kayak CAN definition)
SYM(Symbol file)
ARXML (Autosar XML)
CDD(CAN dela studio diagnistic description)

---
File parsing
>>> import cantools
>>> db = cantools.database.load_file('tests/files/dbc/motohawk.dbc')

---
CAN message encoding and decoding.
Encoding a message and sending it on a can bus :
>>> import can
>>> can_bus = can.interface.Bus('vcan0', bustype='socketcan')
>>> data = message.encode({'Temperature': 250.1, 'AverageRadius': 3.2, 'Enable': 1})
>>> message = can.Message(arbitration_id=message.frame_id, data=data)
>>> can_bus.send(message)

---
Receives a message from the CAN bus and decoding it :
>>> message = can_bus.recv()
>>> db.decode_message(message.arbitration_id, message.data)

---
COMMAND LINE TOOL
- The dump subcommand
  Dump command given database(DBC) in a human readable format:
  $ cantools dump (location of the dbc file)
- Eg:
  $ cantools dump tests/files/dbc/motohawk.dbc

---
- Generate C source subcommand
  This command will Generate C source code from given database (DBC) file.
  $ cantools generate_c_source (location)
- Eg:
  $ cantools generate_c_source tests/files/dbc/motohawk.dbc
  Successfully generated motohawk.h and motohawk.c.

---
- Here we use --database-name to set a custom namespace for all generated types, defines and functions. The output file names are also changed by this option.
  $ cantools generate_c_source --database-name (name) (location)
- Eg:
  $ cantools generate_c_source –database-name my_code Basic_DBC.dbc

---
- Here we use --no-floating-point-numbers to generate code without floating point types,
  $ cantools generate_c_source –no-floating-point-numbers (loc)
- Eg:
  $ cantools generate_c_source --no-floating-point-numbers tests/files/dbc/motohawk.dbc

---
- The monitor subcommand
  It is used to Monitor CAN bus traffic in a text based user interface.
  $ cantools monitor (location of dbc file)
- Eg:
  $ cantools monitor tests/files/dbc/motohawk.dbc

---
load_file
when using a DBC file in a python script , we use this load_file command to import the DBC file
>>> db = cantools.database.load_file('foo.dbc')

---
dump_file
When importing a dbc file , we assign in to some other storage space(variable) .. If we want to add some more files to the same variable , dump_file command is used.
>>> db = cantools.database.load_file('foo.dbc')
>>> cantools.database.dump_file(db, 'bar.dbc')

---
- Cantools to extract the list of messages from the DBC
  get_message_by_frame_id(id)
  get_message_by_name(name)
- Eg:
  msg=db.get_message_by_name('BrakeMsg')
  msg=db.get_message_by_name(0x011)

---
Refresh()
Refresh the internal database state.
This method must be called after modifying any message in the database to refresh the internal lookup tables used when encoding and decoding messages.
Eg:
>>Refresh(‘foo.dbc’)

---
- signal_tree
  All signal names and multiplexer ids as a tree. Multiplexer signals are dictionaries, while other signals are strings.
- Eg:
  db=cantools.db.load_file('/home/gayathri/Basic_DBC.dbc')
   msg=db.get_message_by_name('AirbagMsg')
   print(msg.signal_tree)

---
- is_multiplexed()
  >>> foo = db.get_message_by_name('Foo')
  >>> foo.is_multiplexed()
- Returns either true or false

---
Multiplexing the message in DBC
It is a method for sending data that does not fit into the 8 byte CAN payload. In some cases, it might be best to send it as multiple messages. One signal in the frame is used as a multiplexer and the remaining payload is interpreted depending on the value of the multiplexer signal.

---
TESTER
>>> import can
>>> import cantools
>>> can.rc['interface'] = 'socketcan'
>>> can.rc['channel'] = 'vcan0'
>>> can_bus = can.interface.Bus()
>>> database = cantools.database.load_file('tests/files/tester.kcd')
>>> tester = cantools.tester.Tester('PeriodicConsumer', database, can_bus, 'PeriodicBus')

---
- Start()
  Start the tester. Starts sending enabled periodic messages.
  >>> tester.start()
- Stop()
  Stop the tester. Periodic messages will not be sent after this call. Call start() to resume a stopped tester.
  >>> tester.stop()

---
Messages
Set and get signals in messages. Set signals takes effect immediately for started enabled periodic messages.
>>> periodic_message = tester.messages['PeriodicMessage1']
>>> periodic_message
{'Signal1': 0, 'Signal2': 0}
>>> periodic_message['Signal1'] = 1
>>> periodic_message.update({'Signal1': 2, 'Signal2': 5})
>>> periodic_message
{'Signal1': 2, 'Signal2': 5}

---
- enable(message_name)
  Enable given message message_name and start sending it if its periodic and the tester is running
  >>> tester.enable('PeriodicMessage1')
- disable(message_name)
  Disable given message message_name and stop sending it if its periodic, enabled and the tester is running.
  >>> tester.disable('PeriodicMessage1')

---
Messages
>>> periodic_message = tester.messages['PeriodicMessage1']
>>> periodic_message
{'Signal1': 0, 'Signal2': 0}
>>> periodic_message['Signal1'] = 1
>>> periodic_message.update({'Signal1': 2, 'Signal2': 5})
>>> periodic_message
{'Signal1': 2, 'Signal2': 5}

---
- enable(message_name)
  >>> tester.enable('PeriodicMessage1')
- disable(message_name)
  >> tester.disable('PeriodicMessage1')
- flush_input()
  Flush, or discard, all messages in the input queue.